## Slide 1: Cummins Guidanz™ Mobile Service Feature Training
Public

## Slide 2: Table of Contents
General app information
  New Release Information
  Hardware Requirements
  Download/Installation
  Supported Adapters
General Usage
Service Features
Questions or Issues

## Slide 3: Cummins Guidanz
Guidanz™ is Cummins' new suite of genuine service products, features and capabilities. https://cumminsengines.com/guidanz
Guidanz mobile app includes INSITE like capability and combines everything from diagnostics, training, repair, warranty, metrics and performance feedback
Guidanz app is available for download in US, Canada, Australia, EU (including UK), Mexico, Peru, Columbia, India, and China

## Slide 4: Version 5.2.0 Release
Public
What's new:
New features
Calibration import over email
Immediate Assessment for Multi-ECM products
CARB – messages added to ECM Images
Diagnostic Tests:
  No New Diagnostic Tests
Advanced Features:
  Aftertreatment Maintenance
  Fuel Injector Reset
  Fuel System Performance Monitor
  Maintenance Monitor
  Real Time Clock
  Engine Abuse History
  Idle Shutdown Override
All Features dependent upon the subscriber's user level, and availability in the connected engine

## Slide 5: Hardware Requirements
Public
IOS
  Bluetooth compatible devices only
  iPhone 8, iPad (8th generation), and newer
  Minimum space requirements: 1 GB
  Recommended space requirements: 2 GB
Android
  Minimum OS: Android 7.1 or higher
  Bluetooth compatible devices only
  Minimum RAM: 2 GB
  CPU Architecture: ARMv8-A
  64-bit OS and processor only
  Minimum space requirements: 1 GB
  Recommended space requirements: 2 GB

## Slide 6: Download/Installation
Free Download
  Android
    Search for “Cummins Guidanz” on Google Play
  iOS
    Search for “Cummins Guidanz” on the App Store
Public

## Slide 7: Supported Adapters
INLINE 7
  Has Wired/Wi-Fi/Bluetooth capability
    Guidanz limited to Bluetooth mode
  Works with INSITE as well
INLINE Mini
  Bluetooth
More information about Adapters
https://www.cummins.com/parts-and-service/digital-products-and-services/inline
How to purchase adapters?
  For Cummins internal employees (non-Distributor) go to Ariba, use non-catalog items and order the part using part number and enter MDC as the supplier
  End users can contact their local Cummins distributor or purchase directly from https://store.cummins.com/
Public

## Slide 8: Supported Products
2007 and later Engines
  List of unsupported devices is available on the user guide at Here
ADEPT Route Parameter Manager (RPM) Module
  For More info
    https://www.cummins.com/support/digital-products-and-services-support/adept-support
    Note: Currently you do not need a subscription to service the RPM module.

## Slide 9: General Functionality

## Slide 10: Log-In Screen
All users need to have a valid Cummins user name and password. If not, users can click on the “register now” link or they can register at https://mylogin.cummins.com/web/IAM_NewRegistration?appid=a1a4N00000F2oKa
  Email login for user name in Email format
  Corporate login for users with a WWID
  Legacy Email login for which Email login does not work
After successful Login users will need to set a PIN code and accept the EULA Terms and Conditions to land on Home page.

## Slide 11: Log-In Screen
If a user registered in China wants to log into the Guidanz Mobile app, the user needs to change the region by clicking on the change link before login for authentication

## Slide 12: PIN Creation
User is prompted to set a PIN code and then to confirm his/her entry
New PIN security rules
  PIN must be at least 6 numbers and can be up to 16 numbers long.
  The PIN cannot be an entire sequence of numbers such as 123456 or 654321
  The entire PIN cannot be a sequence that simply repeats two digits like 121212
  You cannot repeat any single number 4 or more times, such as 000012
  Try not to use easily guessed sequences of numbers such as your birthdate, address, or phone number
Public

## Slide 13: Subscription Expiration Notification
The app will display a notification of active subscriptions expiring within 14 days and expired subscriptions.
Public

## Slide 14: Subscription Management
Subscription Management
The user can see All Active Subscriptions
To access Subscription Management:
Settings & Preferences  Account Management  Select the user under Profiles And Accounts 
Select the User 
Subscription Management
Public

## Slide 15: Intapp & Intapp OEM (ECM Password Removal)
Intapp and Intapp OEM units allows users to remove Master, Adjustment, Reset, Anti-theft and OEM passwords.
Both units are purchased through the marketplace.
To view available counts
  Go to Settings & Preferences  Account Management  Select the user under Profiles And Accounts  Select the User  Intapp Unit Management or Intapp OEM Unit Management

## Slide 16: Intapp & Intapp OEM (ECM Password Removal)
Intapp Units and Inatpp OEM Units can be moved between the users online account and their specific devices.

## Slide 17: Cal Assist (Fleet Counts)
Changing the Base Calibration requires the use of a “CalAssist Unit”. These counts can be purchased from your distributor or the Cummins Marketplace
To view available counts
  Go to Settings & Preferences  Account Management  Select the user under Profiles And Accounts  Select the User  CalAssist Unit Management

## Slide 18: Home Page/Start Page
  After logging in, user will see the Home page.
Note: When the user is on the Home Page/Start Page, the Guidanz Mobile app is disconnected from the ECM.
Note: Features displayed on the Home page are dependent upon the user’s subscription level.
  Another way to get to the Home page is by clicking on Menu  Start while performing any action at which time the Guidanz Mobile app will be disconnected from the ECM.
Public

## Slide 19: Menu – Contact Cummins/Log File
Allows user to call or email technical support.
On the Start page, click on Contact Cummins.
The email contains device details and attaches a log file that will help the support personnel troubleshoot issues.
Public

## Slide 20: Menu – Contact Cummins/Log File
Or when connected, click on Menu  Contact Cummins  Email
The email contains device details and attaches a log file that will help the support personnel troubleshoot issues.
Public

## Slide 21: Menu - Settings and Preferences
To access Settings and Preferences:
On the Start page, click on the Settings button
When connected, click on Menu  Settings
Public

## Slide 22: Menu - Settings and Preferences
Change Storage Limits (only for subscribed users)
Allows user to change storage limit for Assessment History, Trim Recovery File, and Calibration Files.
Public

## Slide 23: Connecting Adapter to Guidanz
  When pairing an adapter for the first time in Android OS Guidanz must be able to access the mobile device’s location.
  If device location is not enabled, the user will be prompted to update Location Settings.
Public

## Slide 24: Connecting Adapter to Guidanz
  For initial pairing the adapter must be put in pairing mode
    Hold the reset button at the end of the adapter for about 2-3 seconds
    The light on the adapter will flash for about 2 minutes
    You must pair the adapter to the mobile device within that time
  Subsequent connections
    The mobile device will find the adapter without needing to press the reset button on the adapter
    For Android, the app will display the last connected adapter first and then search for the remaining adapters
  The adapter can be identified by the last few digits of the serial number on its label
Android
Pairing screen is in the app
IOS
Pairing and connection is done on the mobile device’s Bluetooth settings window
Public

## Slide 25: Connecting Adapter to Guidanz
    The Guidanz mobile app does not auto connect to the adapter.
    Unlike some adapters in the market the INLINE 7 and INLINE mini do not auto connect to the mobile device after the initial connection. This is by design to prevent unintended auto connection in locations where multiple users share the adapters.
Android
Pairing screen is in the app
IOS
Pairing and connection is done on the device’s Bluetooth settings window
Public

## Slide 26: Connecting Adapter to Guidanz
  INLINE Mini Firmware Updates
    The INLINE Mini is configured to perform automatic firmware updates. When a user connects to an INLINE Mini in Guidanz Mobile if the app detects a necessary firmware update it will be made automatically and the app will display an Adapter Updated status.
    The INLINE Mini will need to be reconnected to the Guidanz Mobile app following a firmware update.
Public

## Slide 27: Connecting Adapter to Guidanz
  Firmware Update of INLINE 7
    There are 2 options for updating firmware on an INLINE 7 adapter
    Use Cummins Update Manager to update existing INLINE 7 drivers and firmware
    Download the latest INLINE 7 drivers and firmware from
    https://www.cummins.com/support/digital-products-and-services-support/inline-support
    Note: The user will need admin rights to install the INLINE 7 drivers from the website
  After installing the new INLINE 7 driver on the PC, the user will need to connect to an ECM using INSITE (or any other electronic software) to upgrade the firmware. The user will be prompted to update the firmware automatically.
Public

## Slide 28: Share Button
  User can share the content of the screen via email
Public

## Slide 29: Connection Button
  The connection tab in the chyron/footer on each screen brings up a chyron drawer which allows a user to change adapter or disconnect from the adapter
Public

## Slide 30: Manual Refresh
No separate refresh button
Users can manually refresh by swiping down the mobile device screen
Public

## Slide 31: Calibration Import from mail
Compatible calibrations can be imported directly from the mobile device email.
Share the calibration
with Guidanz
to begin the process

## Slide 32: Service Features
Public

## Slide 33: Home Page
To check for Service functionalities, click on the Analyze Equipment button which will connect the user to the ECM.
Public

## Slide 34: Multi-Level Security
If master password is set, user will be prompted for password.
Public

## Slide 35: Intapp Password Removal
If Master, Adjustment, Reset, or Anti-Theft password is set, a standard Intapp can be used to remove the password
If the OEM or OEM2 password is set, an Intapp-OEM can be used to remove the password
Click on the top right Menu  go to Manage Passwords or Unlock Device  Select Remove Passwords
Public

## Slide 36: Intapp Password Removal
Select the appropriate type of Intapp required to unlock the password.
Tap the Agreement checkbox and then tap the Remove Passwords button which will take the user through the Key On/Key Off process.
Public


## Slide 37: User Input Screens
When clicking on Analyze Equipment, user connects the adapter to the truck and pairs to the adapter via the app
The app pulls up Engine Serial Number, and Customer Name from ECM, and the user can edit them if they are incorrect
The user can also enter the Customer Unit Number, the Odometer or Engine hours, a complaint or other notes.
The Event Number to later retrieve the information in History and Templates is also displayed

## Slide 38: User Input Screens
Based on the confirmed ESN, the equipment make and model list is retrieved from the server.
App pre-selects the data received from warranty data on the server and from the ECM if available, but the user has to make a selection.
If there is no manufacturer list, it can be caused by:
  No data based on the ESN provided
  No Internet
  Server issue

## Slide 39: ECM Image Creation
During input, user can also select whether to create an initial ECM image or not by selecting or deselecting the checkbox.
ECM images are created at the beginning and end of a connection to the ECM.
During ECM image creation user can cancel out of ECM image creation by clicking on Cancel button.
ECM image creation can also be enabled or disabled in Settings. Go to Settings & Preferences  Account Management and check or uncheck the Create ECM Image checkbox.
ECM images are saved in the History and Templates folder which can be accessed through the Home screen.

## Slide 40: Engine Serial Number (ESN) Eligibility Check
If the ESN entered in User Input screen is eligible for a cal campaign, Guidanz mobile will notify the user of the availability of a calibration campaign calibration.
To get to the Equipment Summary screen, click on Install Later.
Public

## Slide 41: Equipment Dashboard (Equipment Summary Screen)
The equipment summary screen will show in different sections (if available):
  Equipment Dataplate
  Cummins Engines
    Engine #1
  Public Cummins Devices,
    Route Parameter Manager
    Acumen On-Board Data Logger
    Smart Devices, etc.
  Other Devices
    Transmission
    Brake Controller, etc.
A yellow indicator will show unsupported devices (e.g. Rombooted devices)
User can also get to the Equipment Dashboard by selecting Dashboard in the Menu button once user is in the Device Dashboard

## Slide 42: Equipment Dataplate
Equipment Dataplate can be accessed via the ECM Device Dashboard and Engine Dataplate
It contains the information the user enters such as customer name, manufacturer, model, etc., as well as other information

## Slide 43: Device Dashboard
Clicking on a device on the equipment dashboard displays the device dashboard
The device dashboard screen shows all the functionality that is available for that device

## Slide 44: Engine Dataplate
Engine Dataplate can be accessed via the ECM Device Dashboard
It contains the information read from the ECM, such as ECM information, Calibration information and Equipment information

## Slide 45: ECM Fault Screens
Clicking on Faults on the ECM Device Dashboard displays the Faults and Analysis screen with primary faults, unprioritized faults, and related faults
Clicking on an individual Cummins fault code displays the Fault Details and, if supported, the fault snapshot
Clicking on a fault code number will open the respective Fault Information System (FIS) file in a web browser

## Slide 46: Clear Fault Codes
To clear fault codes, click on the right-hand top Menu option and select Clear All Faults
After user confirms to Clear Faults Now, app continues to Key Off/Key On process
At the end of the process, app confirms Faults cleared successfully
If user Cancels, no faults will be cleared

## Slide 47: Field Repair Actions
Field Repair Actions display the list of open Temporary Repair Practices (TRP) and Campaigns for the ESN of the connected engine.
Once user clicks on Field Actions the number of available Campaigns and TRPs will be displayed.

## Slide 48: Data Monitor Logging (DML)
Clicking on Data Monitor on the ECM Device Dashboard takes the user to the Data Monitoring screen which allows the user to monitor and record parameters
When clicking on Monitor the user can monitor all parameters while ECM is running

## Slide 49: Data Monitor Logging (DML)
When clicking on the green button, the Data Monitoring control screen is opened
The user can start and pause (stop) DML and change the time settings
When clicking on the Record button the user can record the parameters
While recording, each time the user clicks the Pause button or leaves the DML screen a record file is created and stored.

## Slide 50: Data Monitor Logging (DML)
A user can use pre-defined groups with pre-defined parameters to monitor or record
A user can create and save a new custom group with parameters user selects (the parameters that are not currently supported are grayed out)
A user can add custom or pre-defined groups to Favorites

## Slide 51: Engine Settings
Clicking on Engine Settings on the ECM Device Dashboard the user is taken to the Engine Settings screen where the user can see the values of each parameter.
User can view and edit System ID and Dataplate settings by clicking on System ID and Dataplate in the Engine Settings screen

## Slide 52: Engine Settings
User can search the Engine Settings parameter list
User can change parameter and sub-parameter values that are not locked by changing the value within the specified min and max values

## Slide 53: Engine Settings
After user confirms the changes, user can save changes
Changes are written to ECM by going through Key Off/Key On process
At the end of the process, saved changes are confirmed
If you move away from the screen without saving, the changes will be discarded

## Slide 54: Calibrate Engine
The Calibrate Engine feature on the ECM Device Dashboard will display to the user whether or not the installed ECM code is up to date or whether there is a new revision of the ECM code available.

## Slide 55: Calibrate Engine
If there is a new ECM code available, and the user clicks on the Calibrate Engine feature on the ECM Device Dashboard, the user will be taken through the process to upgrade to the latest ECM code revision.
Only for an ESN in campaign, if the calibration download fails or the ECM gets rombooted during the calibration download, the user can recover the ECM by going through the pre-defined steps using the same device and user login.

## Slide 56: Calibrate Engine
Selecting “Calibrate Engine” will allow users to see calibrations on the device, and download new calibrations from the cloud.

## Slide 57: Calibrate Engine
Calibrations are stored on the device can be used to update or change the calibration of an ECM

## Slide 58: Calibrate Engine – Cal Assist
Changing the Base Calibration requires the use of a “CalAssist Unit”. These counts can be purchased from your distributor or the Cummins marketplace

## Slide 59: Calibration Installation Process
The app will go through Steps 1 - 4 of the installation process.
Public

## Slide 60: Calibration Installation Process
The app will go through Steps 1 - 4 of the installation process.
Public

## Slide 61: Key Off Instructions
After completion of the 4 installation steps, the user is prompted to key off. A timer will count down. Its length is determined by the engine type.
Public

## Slide 62: Key On Instructions
After the timer reaches 0, the user is prompted to key back on, at which time the app is reconnecting to the ECM.
Public

## Slide 63: Calibration Installation Success
The app will inform the user whether the installation was successful.
Public

## Slide 64: Advanced Features
Clicking on Advanced Features on the ECM Device Dashboard the user is taken to the Advanced Features screen where the user can see the supported Advanced Features.
If supported by the calibration, following Advanced Features have been implemented:
  Engine Protection
  Duty Cycle Monitor
  SAE J1939 Powertrain Control
  SAE J1939 Multiplexed Fault Data
  Engine Torque History
  Aftertreatment History
  Aftertreatment Particulate Matter Sensor Regeneration
  Aftertreatment SCR Catalyst Cold Soak Override
  Aftertreatment SCR Maintenance
  Aftertreatment SCR Regeneration History
  Immobilizer Installation
  Rated Overspeed Protection
  Stop Start Active Inhibit Monitor
User can also manage Advanced Features by adding them to the Favorites list.

## Slide 65: Advanced Features – ECM data Extraction
From the Advanced Features screen where the user can see the supported Advanced Features, select ECM Data Extraction
The ECM Data Extraction process can take up to 20 minutes to complete

## Slide 66: Diagnostic Tests
Clicking on Diagnostic Tests on the ECM Device Dashboard the user is taken to the Diagnostic Tests screen where the user can see all the diagnostic tests implemented in the Guidanz Mobile app and if supported by the calibration.

## Slide 67: Diagnostic Tests
  Cylinder Cut-out Test
  Fan Override Test
  Solenoid Click Test
  Engine State Monitor
  Aftertreatment SCR System Test (SPT2)
  Electronic Fuel Control Actuator Override Test
  Aftertreatment Current Based Particulate Matter Sensor Regen
  Injector Check Valve Diagnostics Test
  Aftertreatment Diesel Exhaust Fluid System Leak Test
  Starter Lockout Relay Driver Override Test
  Intake Air Heater Override
  Aftertreatment Diesel Particulate Filter Regeneration Test
  Fuel System Leakage Test
  Diesel Exhaust Fluid Doser Pump Override Test
  Fast Idle Warmup Test
  VGT Hysteresis Test
  High NOX reset
  Fuel Level Override Test
  Fuel Injector Performance Test
  Electric Fuel Lift Pump Override Test
  Aftertreatment Diesel Particulate Filter Restriction Test
  Aftertreatment Diesel Exhaust Fluid Pump Heater
  Aftertreatment SCR Catalyst Desulphurization
Implemented diagnostic tests (if supported by calibration in ECM)

## Slide 68: Diagnostic Tests
  Switch and Sensor Intermittent Connection Test
  Aftertreatment Diesel Exhaust Fluid System Leak Test
  Aftertreatment Diesel Particulate Filter Deep Clean Regeneration
  Aftertreatment SCR performance test.
  Aftertreatment SCR System cleaning test
  Cylinder Performance Test​
  Gas Throttle Control Test
  SAE J1939 Datalink Control Test
  Engine Protection Witness Test
  Setup for Dynamometer
  Diesel Exhaust Fluid Doser System Heater Test
Implemented diagnostic tests (if supported by calibration in ECM)
  VGT Electronic Actuator Install and Calibration
  Cylinder Bank Cutout Test
  Engine Fuel Supply Pump Override Test
  Engine Priming Pump Override
  Heated Oxygen Sensor Test
  High Pressure Fuel System Actuator Override Test
  Open Loop Mode Lock-In Test
  Shut Off Valve Solenoid Actuator Test
  Single Bank Cutout Test
  Aftertreatment Hydrocarbon Doser System Test
  Charge Throttle Actuator Test
  Fuel Control Valve Test

## Slide 69: Diagnostic Tests
Implemented diagnostic tests (if supported by calibration in ECM)
  Aftertreatment Engine Out NOx Sensor Test
  Aftertreatment Inducement Witness Test.
  Aftertreatment System Out NOx Sensor Test
  Compressor Bypass Valve Test
  EGR Delta Pressure Auto Zero Test
  Exhaust Throttle Auto Zero Test

## Slide 70: Diagnostic Tests
When clicking on a specific diagnostic test in the Diagnostic Tests screen the user is taken to the selected diagnostic test with instructions, possibly indicators with check boxes, and the status box.
The user should follow the pre-conditions outlined in the Instructions section before trying to start any diagnostic test in order to avoid any issues with starting or running the diagnostic test.

## Slide 71: Diagnostic Tests
The user can go to the diagnostic test controls screen by clicking on the red button in the Chyron

## Slide 72: Diagnostic Tests
The Diagnostic Test Controls chyron allows the user to start and stop the test
The Status box displays the diagnostic test status.

## Slide 73: Trip Information
Clicking on Trip Information on the ECM Device Dashboard the user is taken to the Trip Information screen where the user can chose the required trip information
User can enable the trip fuel report
User can reset the trip information

## Slide 74: Images & Templates
Clicking on Images & Templates on the ECM Device Dashboard the user is taken to the Images and Templates screen where the user can manage available Images or Templates
Clicking on Images shows all captured images for the connected ESN
User can also search the Images or change the Sort order

## Slide 75: Images & Templates
Clicking on an image allows the user to connect to the ECM image which disconnects the user from Engine #1
Clicking on the three dots on the left-hand side of the ECM image allows the user to Convert to Template, Share EIF File, and Delete File
Currently, ECM images created in INSITE can be imported into Guidanz Mobile app, but ECM images created in Guidanz Mobile app cannot be imported into INSITE

## Slide 76: Images & Templates
When user selects to convert image to template, user can change template name and enter template notes
Once the template has been created successfully, the user can write it to the ECM
The user is then taken through the Key Off/Key On process to save the template to the equipment

## Slide 77: Images & Templates
To send an image to another user, in History and Templates click on Images
Go to the image user wants to share
Click on the three dots to the left of the image
Select Share EIF File
Select the default email client to send to another user

## Slide 78: Images & Templates
To receive a image to import into Guidanz Mobile app, open an email client
Select the email and click on the image in eif format
If available, click on Copy to Guidanz, or search for the app through More options to import
The user is then asked to Import

## Slide 79: Images & Templates
User will then see Image Properties
User can change ECM Image name and Technician Notes
If image was imported successfully, user will receive a notification

## Slide 80: Audit Trail
Clicking on Audit Trail on the ECM Device Dashboard the user is taken to the Audit Trail screen where the user can see the audit trail of the connected ECM

## Slide 81: Calibration Files – Viewing calibrations on the device
Selecting “Calibration Files” will allow the user to view calibrations, the revision history, properties, and delete calibrations that have been downloaded to the device.

## Slide 82: Calibration Files - Search
Selecting “Search Online” will allow the user to enter a base calibration and search for the latest revision.

## Slide 83: Calibration Files – Download to device
After searching, users have the option to view the revision history, or download the calibration to their device.

## Slide 84: History and Templates (Event Folder)
User can access the History and Templates folder from the Home screen. The user can go to History and Templates and find
ECM Images
Templates
In each work order, user can find
ECM Images
DML Log files
Calibration Log File
Trim Recovery File
which can be shared or deleted by the user.
Public

## Slide 85: Device notifications
If the user gets locked out during an operation, both the device and the app will inform the user of the operation through background notification.
Public

## Slide 86: Auto-Update of the app
In iOS:
  Go to Settings and Enable the Updates option
In Android:
  Open Google Play app
  Activate the Auto-update apps option
Public

## Slide 87: Engines not supported
Engine Program | ECM |  | Engine Program | ECM
480C-E | CM552 |  | ISM | CM570
B5.9G | CM420 |  | ISM - CM870 | CM870
C Gas Plus/B Gas Plus | CM556 |  | ISM - CM875 | CM875
C8.3G | CM420 |  | ISM - Fuel Control Module - CM570 | CM570
CELECT | ECM-B |  | KTA19, G855 CM558 G Drive | CM558
CELECT Plus | ECM-C |  | L Gas Plus | CM556
CELECT Plus Industrial | ECM-C |  | L10G | CM420
Centinel | CM400 |  | PIM | CM550
CENTRY | CM400 |  | QSB5.9/44, 5.9/30, 4.5/30, 3.9/30 | CM550
Gas Compression GTA3.9/5.9/8.3GC, KTA19/38GC - SSM558/CM556/CM2358 | CM556 |  | QSC8.3/QSL9 | CM554
 | SSM558 |  |  | CM500
ISB | CM550 |  | QSK19/23/45/60/78 | CM500
ISB - CM850 | CM850 |  | QSK19G/38G/60G, QSV81/91 - CM700/SSM558/CM2358 | CM700, SSM558
ISB Daimler Chrysler | CM551 |  |  | CM2358
ISBe (4 and 6 Cylinder) | CM800 |  | QSM11 | CM570
ISBe2/3 - CM850 | CM850 |  | QST30 | CM552
ISBe4 (4 and 6 cylinder) | CM850 |  | QST30 - Power Gen | CM552
ISC / Transit Bus ISL8.3 - CM850 | CM850 |  | QSX15 | CM570
ISC/ISL | CM554 |  | Signature/ISX | CM570
ISL8.9 - CM850 | CM850 |  | Signature/ISX - CM870 | CM870
ISLe4 (6 cylinder) | CM850 |  |  | 

## Slide 88: Questions or Issues
Please contact Cummins Care for any questions or issues
  Call: 1-800-CUMMINS
  Email: ServiceToolSupport@cummins.com
  Chat Service: www.cummins.com
  Tool Support Website: www.cummins.com
Public