## Slide 1: Cummins Guidanz™ Mobile Immediate Assessment and Guest User Training
Public

## Slide 2: Table of Contents
General App Information
  Cummins Guidanz
  Functionality
  Supported Products
  Hardware Requirements
  Supported Adapters
General Functionality
Basic Functionality
Immediate Assessment

## Slide 3: Cummins Guidanz
Guidanz™ is Cummins' new suite of genuine service products, features and capabilities. https://cumminsengines.com/guidanz
Guidanz mobile app includes INSITE like capability and combines everything from diagnostics, training, repair, warranty, metrics and performance feedback
Guidanz app is available for download in US, Canada, Australia, EU (including UK), Mexico, Peru, Columbia, India, and China

## Slide 4: Version 5.2.0 Release
Public
What's new:
New features
Calibration import over email
Immediate Assessment for Multi-ECM products
CARB – messages added to ECM Images
Diagnostic Tests:
  No New Diagnostic Tests
Advanced Features:
  Aftertreatment Maintenance
  Fuel Injector Reset
  Fuel System Performance Monitor
  Maintenance Monitor
  Real Time Clock
  Engine Abuse History
  Idle Shutdown Override
All Features dependent upon the subscriber's user level, and availability in the connected engine

## Slide 5: Hardware Requirements
Public
IOS
  Bluetooth compatible devices only
  iPhone 8, iPad (8th generation), and newer
  Minimum space requirements: 1 GB
  Recommended space requirements: 2 GB
Android
  Minimum OS: Android 7.1 or higher
  Bluetooth compatible devices only
  Minimum RAM: 2 GB
  CPU Architecture: ARMv8-A
  64-bit OS and processor only
  Minimum space requirements: 1 GB
  Recommended space requirements: 2 GB

## Slide 6: Download/Installation
Free Download
  Android
    Search for “Cummins Guidanz” on Google Play
  iOS
    Search for “Cummins Guidanz” on the App Store
Public

## Slide 7: Supported Adapters
INLINE 7
  Has Wired/Wi-Fi/Bluetooth, but Guidanz only works in Bluetooth mode
  Works with INSITE as well
INLINE Mini
  Bluetooth
More information about Adapters
https://www.cummins.com/support/digital-products-and-services-support
How to purchase adapters?
  For Cummins internal employees (non-Distributor) go to Ariba, use Non-catalog items and order the part using part number and enter MDC as the supplier
  Distributors and dealers can purchase it directly from https://store.cummins.com/
  For all others, users need to contact their local distributor

## Slide 8: Supported Products
2007 and later Engines
  List of unsupported devices is available on the user guide at Here
ADEPT Route Parameter Manager (RPM) Module
  For More info
    https://www.cummins.com/support/digital-products-and-services-support/adept-support
    Note: Currently you do not need a subscription to service the RPM module.

## Slide 9: General Functionality

## Slide 10: New Log-In Screen
All users need to have a valid Cummins user name and password. If not, users can click on the “register now” link or they can register at https://mylogin.cummins.com/web/IAM_NewRegistration?
  Email login for user name in Email format
  Corporate login for users with a WWID
  Legacy Email login for which Email login does not work
After successful Login users will need to set a PIN code and accept the EULA Terms and Conditions to land on Home page.

## Slide 11: New Log-In Screen
If a user registered in China wants to log into the Guidanz Mobile app, the user needs to change the region by clicking on the change link before login for authentication

## Slide 12: PIN Creation
User is prompted to set a PIN code and then to confirm his/her entry
New PIN security rules
  PIN must be at least 6 numbers and can be up to 16 numbers long.
  The PIN cannot be an entire sequence of numbers such as 123456 or 654321
  The entire PIN cannot be a sequence that simply repeats two digits like 121212
  You cannot repeat any single number 4 or more times, such as 000012
  Try not to use easily guessed sequences of numbers such as your birthdate, address, or phone number
Public

## Slide 13: Subscription Expiration Notification
The app will display a notification of active subscriptions expiring within 14 days and expired subscriptions.
Notes: Separate line items among screen buttons

## Slide 14: Subscription Management
Subscription Management
The user can see All Active Subscriptions
To access Subscription Management:
Settings & Preferences  Account Management  Select the user under Profiles And Accounts 
Select the User 
Subscription Management

## Slide 15: Connecting Adapter to Guidanz
  For Initial Pairing, the adapter has to be put on pairing mode
    Hold the reset button at the end of the adapter for about 2-3 seconds
    The light on the adapter will flash for about 2 minutes
    You have to pair it to the device within that time
  Subsequent connections
    The device would be able to find the adapter without needing to press the button on the adapter
  The adapter can be identified by the last few digits of the s/n on the label
Android
Pairing screen is within the app
IOS
Pairing and connection is done on the devices Bluetooth settings window

## Slide 16: Connecting Adapter to Guidanz
  Known Issue
    This is not a bug.
    App does not auto connect to the adapter.
    Unlike some adapters in the market the INLINE 7 and INLINE mini do not auto connect to the mobile device after the initial connection. This is by design to prevent unintended auto connection in locations where multiple users share the adapters.
    We are investigating if something can be done to make it easier to the user, while we (Cummins) must keep our security protocol in place.
Android
Pairing screen is within the app
IOS
Pairing and connection is done on the devices Bluetooth settings window

## Slide 17: Connecting Adapter to Guidanz
  Firmware Update of INLINE Mini
    If the firmware of the INLINE Mini needs to be updated, once you have selected the INLINE Mini adapter in the app, the app will automatically update it and display a status update once completed.
    If a firmware update has been completed, please be aware that you will have to reconnect again the INLINE Mini.

## Slide 18: Home Page/Start Page
  After logging in, user will see the Home page.
Note: When the user is on the Home Page/Start Page, the Guidanz Mobile app is disconnected from the ECM.
Note: Features displayed on the Home page are dependent upon the user’s subscription level.
  Another way to get to the Home page is by clicking on Menu  Start while performing any action at which time the Guidanz Mobile app will be disconnected from the ECM.
Public

## Slide 19: Menu - Settings and Preferences
To access Settings and Preferences:
In the Start page, click on the Settings button
When connected, click on Menu  Settings

## Slide 20: Menu - Settings and Preferences
ACCOUNT
Account Management - Allows user to view subscription status, change pin, remove user profiles, add new users, enable/disable background/foreground locks and time, change PIN
CONNECTIVITY
Add New Adapter - Allows user to add a new adapter
Change Active Adapter - Allows user to add a new adapter
Change Storage Limits – Allows user to change the duration IA records are stored for. By default they are stored for 30 days.
PREFERENCES
Notifications - Allows user to enable/disable onscreen notification when the adapter goes out of range or when a time consuming task(like calibration update) is completed
Refresh & Update Defaults – Allows user to set faults and monitor refresh rates
Language – Allows user to change the language
Share Location in Email – Shares location GPS coordinates in email
ABOUT
Cummins Guidanz link – Shows app version and displays intro screen again
Terms of Service – Shows user the End User License Agreement
Privacy Policy – Allows user to see Cummins Inc. Privacy Policy
Feedback – Allows user to contact servicetoolsupport@cummins.com

## Slide 21: Language Settings
Available languages
English
French
Spanish
Simplified Chinese

## Slide 22: Menu – Contact Cummins/Log File
Allows user to call or email technical support.
In Start page, click on Menu  Contact Cummins.
The email contains device details that will help the support personnel troubleshoot issues.

## Slide 23: Menu – Contact Cummins/Log File
Or when connected, click on Menu  Contact Cummins  Email
The email contains device details that will help the support personnel troubleshoot issues.

## Slide 24: Share Button
  User can share the content in the screen via email

## Slide 25: Sharing Fault Results
User can click the “Share” button from the Faults screen or from the Immediate Assessment summary page to email the results
Emailing from either page will share the same results
It appends VIN, ESN, and some other information from the Dataplate and individual fault details page so that the user doesn’t need to go to individual pages and email
“Share” button from any other page will email only the content in that page.

## Slide 26: Location
  When user selects the Location option in Settings in the device, as well as the Share Location in Email in Settings in the app, the device location will be included in the email.

## Slide 27: Connection Button
  Adapter Tab - Allows user to change adapter or disconnect app from adapter

## Slide 28: Manual Refresh
Users can manually refresh the screen by swiping down the screen

## Slide 29: Calibration Import from mail
Compatible calibrations can be imported directly from the mobile device email.
Share the calibration
with Guidanz
to begin the process

## Slide 30: Basic Functionality – Guest User

## Slide 31: Home Page
Basic Functionality
  Campaign Calibration installation capability
  "Scan Fault" which is a focused function that can be used to just read the faults from the engine without any fault prioritization.
  Enter ESN and customer information
  Create Events and View Events
  RPM module support
  Equipment and device dataplate information
  Prioritized Cummins fault codes, and descriptions
    Does not apply to multiple ECM engines
  J1939 Device Fault
  The ability to share any information in the app via email
  French, Spanish, Simplified Chinese language support

## Slide 32: Scan Faults
When selecting Scan Faults the user is taken directly to the Equipment Dashboard
No prioritized fault codes will be displayed
Event folder will be created

## Slide 33: Campaign Calibration Installation Through Analyze Equipment
If the user clicks on Analyze Equipment the user will be taken to the ECM Device Dashboard once the user is connected to the ECM.
Public

## Slide 34: Calibrate Engine
The Calibrate Engine feature on the ECM Device Dashboard will display to the user whether or not the installed ECM code is up to date or whether there is a new revision of the ECM code available.
  Does not apply to multiple ECM engines.

## Slide 35: Calibrate Engine
If there is a new ECM code available, and the user clicks on the Calibrate Engine feature on the ECM Device Dashboard, the app checks whether the ESN is in campaign and then user will be taken through the process to upgrade to the latest ECM code revision.
Only for an ESN in campaign, if the calibration download fails or the ECM gets rombooted during the calibration download, the user can recover the ECM by going through the pre-defined steps using the same device and user login.

## Slide 36: Campaign Calibration Installation
To check for available calibration download, click on the Campaign Calibration Check button which will connect the user to the ECM.
  Does not apply to multiple ECM engines.
Public

## Slide 37: Engine Serial Number (ESN) Eligibility Check
If Guidanz detects an invalid ESN, the user is prompted to enter a valid ESN
Public

## Slide 38: Engine Serial Number (ESN) Eligibility Check
Guidanz mobile will notify the user of the availability or non-availability of a calibration.
If the Engine is not Calibration Campaign eligible, the engine calibration revision can be updated through “Analyze Equipment” path.
Public

## Slide 39: ECM Code Information
If user clicks on Begin Process, after retrieving the calibration data for the connected ECM, the app will display the installed ECM Code and the ECM Code revision.
If the installed ECM Code is already at the latest revision, the user will receive an Up to Date notification that there is no new ECM code to install.
If there is a newer ECM Code revision, the app will prompt the user to Download ECM Code.
Once the user clicks on Download ECM Code the app will validate the revision compatibility and then download the new ECM Code.
Public

## Slide 40: ECM Code Information
After the app has downloaded the latest ECM Code revision from the cloud, or if the ECM Code has already been downloaded and stored on the phone, a message will be displayed that a new ECM Code is ready to install.
The user can also delete the downloaded ECM code at this point.
Public

## Slide 41: User Warning Messages
When the user clicks New ECM Code Ready to Install, the app will display warning messages. The user must read and click Agree, and Install to start the installation process
If the user has to enter a master password to unlock the device, the Risks of Calibration Update warning message will be displayed twice.
Public

## Slide 42: Multi-Level Security
If master password is set, user will be prompted for password.
Public

## Slide 43: Calibration Installation Process
The app will go through Steps 1 - 4 of the installation process.
Public

## Slide 44: Calibration Installation Process
The app will go through Steps 1 - 4 of the installation process.
Public

## Slide 45: Key Off Instructions
After completion of the 4 installation steps, the user is prompted to key off. A timer will count down. Its length is determined by the engine type.
Public

## Slide 46: Key On Instructions
After the timer reaches 0, the user is prompted to key back on, at which time the app is reconnecting to the ECM.
Public

## Slide 47: Calibration Installation Success
The app will inform the user whether the installation was successful.
Public

## Slide 48: Calibration Recovery Process
Prerequisites:
Calibration Recovery only works for ESNs that are in no parts campaign(s).
Calibration Recovery only works when using the same device that was used for original calibration download.
No fleet counts are required for Calibration Recovery.
Public

## Slide 49: Calibration Recovery Process
If there is a loss of communication in Step 1 of 4 of calibration installation, the app will inform the user that the download failed with the option to Try Again. After re-establishing the connection and clicking on Try Again, the calibration download will start again.
Public

## Slide 50: Calibration Recovery Process
If there is a cal download failure in Step 2 of 4 without any loss of communication, the app will inform of the failure status of the module with the option to Try Again.
If there is a loss of communication in Step 2 of 4, the app will inform the user that the download failed with the option to Start Over (Snapshot 2). After reconnecting, you will see Snapshot 1.
At this point, in both cases, the module is ROM booted.
Public
Snapshot 1
Snapshot 2

## Slide 51: Calibration Recovery Process
If there is a cal download failure in Step 3 of 4 or Step 4 of 4 without any loss of communication, the app will inform of the failure status of the module with the option to Ignore and Continue or Try Again.
If there is a loss of communication in Step 3 of 4 or Step 4 of 4, the app will inform the user that the installation failed with the option to Start Over (Snapshot 2). After reconnecting, you will see Snapshot 1.
If the cal recovery does not work, the user can chose to Share the Recovery Files and use INSITE to recover.
At this point, in both cases, the module is up-to-date but few parameters failed to restore.
Public
Snapshot 1
Snapshot 2

## Slide 52: Calibration Recovery Process with INSITE
If any of above prerequisites for calibration recovery process is not met, user has to use INSITE to try to recover a rom-booted ECM.
In Guidanz Mobile app, go to the event folder and find the trim recovery file (ending in .trm). Share the file with a user who has INSITE installed on his computer and the required INSITE subscription.
Save the trim recovery file in the C:\Intelect\INSITE\Cal Logs folder. Connect to the rom-booted ECM and download the same calibration as in the app while using the trim recovery file. A fleetcount will be required.
Public

## Slide 53: Analyze Equipment
When selecting Analyze Equipment the app pulls up Engine Serial Number, and Customer Name from ECM, and the user can edit them if they are incorrect. The user can also enter Customer Unit Number and Odometer/Engine hours and Complaint or Other Notes.
The user is taken directly to the Equipment Dashboard
Faults will be displayed in a prioritized order
  Does not apply to multiple ECM engines
An event folder will be created. The Event Number is being displayed.

## Slide 54: Engine Serial Number (ESN) Eligibility Check
The app will notify the user of the availability of a calibration campaign.
Every time a user connects to an ECM, if a calibration campaign is found a notification of Calibration Campaign Availability will be displayed if the ESN is in campaign.
If user clicks on Begin Process the app will take the user to the Calibration Download process.
If the Engine Serial Number in the ECM is not part of a calibration campaign, there will not be a notification.
If the user wishes to participate in cal campaign field test, please contact CumminsFieldTest@cummins.com.

## Slide 55: Equipment Dashboard (Equipment Summary Screen)
The equipment summary screen will show in different sections (if available):
  Equipment Dataplate
  Cummins Engines
    Engine #1
  Public Cummins Devices,
    Route Parameter Manager
    Acumen On-Board Data Logger
    Smart Devices, etc.
  Other Devices
    Transmission
    Brake Controller, etc.
A yellow indicator will show unsupported devices (e.g. Rombooted devices)
User can also get to the Equipment Dashboard by selecting Dashboard in the Menu button

## Slide 56: Acumen On-Board Data Logger
The ACUMEN On-Board data logger device is supported and allows user detect and display fault and data plate details, and to monitor data.

## Slide 57: Equipment Dataplate
Equipment Dataplate can be accessed via the ECM Device Dashboard and Engine Dataplate
It contains the information the user enters such as customer name, manufacturer, model, etc., as well as other information

## Slide 58: ECM Fault Screens
Clicking on Faults in the ECM Device Dashboard displays the Faults and Analysis screen
Clicking on an individual Cummins fault code displays the Fault Details

## Slide 59: Calibration Files – Viewing calibrations on the device
Selecting “Calibration Files” will allow the user to view calibrations that have been downloaded to the device.

## Slide 60: Calibration Files - Search
Selecting “Search Online” will allow the user to enter a base calibration, search for the latest revision.

## Slide 61: Calibration Files – Download to device
After searching, users have the option to view the revision history, or download the calibration to their device.

## Slide 62: Device Dashboard
Clicking on a device on the equipment dashboard displays the device dashboard
The device dashboard screen shows all the functionality that is available for that device
Core II ECM - Device Dashboard
Currently only “Engine Dataplate” and “Faults” functionality is available
RPM - Device Dashboard

## Slide 63: J1939 Device Dashboard and Faults
Clicking on a J1939 device on the equipment dashboard displays the J1939 device dashboard
The device dashboard for J1939 devices allows you to view the faults and fault details.

## Slide 64: ECM and J1939 Zero Faults
ECM will display 0 No faults found if no faults are detected.
J1939 devices will display No Faults Detected if no faults can be found.

## Slide 65: History and Templates (Event) Folder
Event Folders can be viewed by clicking on History and Templates in the Start screen
Event Folder Details can be viewed by
clicking on an event in the Event Folders screen
clicking on the bottom left icon on the chyron

## Slide 66: Device notifications
If the user gets locked out during the calibration download, both the device and the app will inform the user of the calibration installation through background notification.
Public

## Slide 67: Immediate Assessment – IAM Subscription

## Slide 68: Immediate Assessment
When a truck pulls up to a shop, the service writer pulls up the faults and estimate how long the service will take
Based on the estimated time to service, the truck gets directed to the appropriate service bay
This feature does not apply to multiple ECM engines

## Slide 69: Immediate Assessment Service
  The customer is met in the lot by the Service Writer
  The SW plugs in a datalink adapter and uses a smart phone app (Fault Advisor App) to get public(SPN/FMI) fault code information from the ECM
  QSOL is used to convert the SPN/FMI info into a Cummins fault code
  QSOL FCA is used to prioritize the faults
  The prioritized faults and engine make/model are plugged into a spreadsheet that predicted the Average Repair Time and Root Causes by percentage
Old process
  With the Guidanz App, this process can be done within a few minutes. In addition, a Guidanz web (CSS) job can be created using Immediate Assessment Results to reduce intake on Guidanz web.

## Slide 70: Home Page
Subscribed User Functionality
  Prioritized Cummins fault codes, descriptions, and the top three most likely root causes
  Estimated service times
  Ability to update Guidanz Web Appointments
  Enter ESN and customer information
  Select manufacturer and model
  Equipment and device data plate information
  Create, View, Resume, Delete Events
  RPM module support
  Create a Guidanz Web Job
  J1939 Device Fault
  Campaign Calibration installation capability
  "Scan Fault" which is a focused function that can be used to just read the faults from the engine without any fault prioritization.
  The ability to share any information in the app via email
  French, Spanish, Simplified Chinese language support

## Slide 71: Immediate Assessment Input
When clicking on New Assessment, user connects the adapter to the truck and pairs to the adapter via the app
The app pulls up Engine Serial Number, and Customer Name from ECM, and the user can edit them if they are incorrect
Based on the confirmed ESN, the equipment make and model list is retrieved from the server.
App pre-selects the data received from warranty data on the server and from the ECM if available, but the user has to make a selection.
If there is no manufacturer list, it can be caused by:
  No data based on the ESN provided
  No Internet
  Server issue

## Slide 72: Immediate Assessment Input (continued)
If the user selects ‘Other Manufacturer’, the app prompts the user for the accessibility code
The results are more accurate with manufacturer and model than with accessibility code

## Slide 73: Engine Serial Number (ESN) Eligibility Check
The app will notify the user of the availability of a calibration campaign.
Every time a user connects to an ECM, if a calibration campaign is found a notification of Calibration Campaign Availability will be displayed if the ESN is in campaign.
If user clicks on Continue, the app will take the user to the Equipment Dashboard.
If the Engine Serial Number in the ECM is not part of a calibration campaign, there will not be a notification.

## Slide 74: ECM Fault Screens - Severity
The app displays the severity to show the current condition of the engine based on below color codes:

## Slide 75: ECM Fault Screens – Fast Track Repair Notification
Only if an engine has a fault code which is part of Fast Track Repair (formerly known as Analytic Based Repair), user will be notified that there is a Fast Track Repair available for the associated fault code. User will see the associated solution(s).

## Slide 76: ECM Fault Screens – Optimized Diagnostics ( formerly ADBR)
During the initial IA connection, Guidanz will capture Optimized Diagnostics from the ECM.
Please stay connected to the ECM until the ECM data is successfully extracted for the most accurate estimates.
This will take 5 minutes.

## Slide 77: Immediate Assessment Output
The faults screen displays the following for each prioritized fault
  Typical Service Times for fault (if available)
  Top Likely Root Causes

## Slide 78: Immediate Assessment Output (Continued)
Not all faults will have estimated service time based on manufacturer and model
If estimated service time is not available, the user can select to enter accessibility code
If data is available based on accessibility code, the app will display estimated service time for the faults that didn’t have data before. (It is possible that even with the accessibility code, some faults still may not have estimated service times)
If there are no faults detected, 0 Faults will be displayed.

## Slide 79: Creating Guidanz Web job from Faults and Analysis Screen
When immediate assessment has been performed, the user works for a Guidanz Web location, and there is an Internet connection, the bottom left icon on the chyron will allow the user to Create a Guidanz Job Order.
Selecting Create Guidanz Job Order will initiate the job creation process.
The Guidanz Job Order number, the Event Folder number as well as the Immediate Assessment number are shown
The user can also Make New Immediate Assessment or View Event Folder Details

## Slide 80: Pending Service Requests
User can create an Immediate Assessment from a pending Service Requests.
Pending Service Requests are created in Guidanz Web.

## Slide 81: Updating Guidanz Web job from Faults and Analysis Screen
When immediate assessment has been performed from a pending appointment, the user works for a Guidanz Web location, and there is an Internet connection, the bottom left icon on the chyron will allow the user to Update the Job Appointment.
Selecting Update Job Appointment will update the already existing Job Order in Guidanz Web
The Guidanz Job Order number, the Event Folder number as well as the Immediate Assessment number are shown
The user can also Make New Immediate Assessment or View Event Folder Details

## Slide 82: History and Templates (Event) Folder
An Immediate Assessment will create an Event Folder. Event Folders can be viewed by clicking on View Events in the Start screen
Event Folder Details can be viewed by
clicking on an event in the Event Folders screen
clicking on the bottom left icon on the chyron

## Slide 83: Viewing the Guidanz Web job
To view the Guidanz Web job, go into the respective Event Folder details and click on View Guidanz Job Order Details.
Guidanz web has different links for distributors vs dealers. Clicking on the link will open Guidanz web on a web browser that the user will need to sign into to view the job.
  Distributor (Classic): css.cummins.com/cmi
  Distributor (Evolution): https://guidanzfsl.cummins.com/cmi
    (Chrome is the preferred browser)
  Dealer (Classic): css.cummins.com

## Slide 84: Engines not supported
Engine Program | ECM |  | Engine Program | ECM
480C-E | CM552 |  | ISM | CM570
B5.9G | CM420 |  | ISM - CM870 | CM870
C Gas Plus/B Gas Plus | CM556 |  | ISM - CM875 | CM875
C8.3G | CM420 |  | ISM - Fuel Control Module - CM570 | CM570
CELECT | ECM-B |  | KTA19, G855 CM558 G Drive | CM558
CELECT Plus | ECM-C |  | L Gas Plus | CM556
CELECT Plus Industrial | ECM-C |  | L10G | CM420
Centinel | CM400 |  | PIM | CM550
CENTRY | CM400 |  | QSB5.9/44, 5.9/30, 4.5/30, 3.9/30 | CM550
Gas Compression GTA3.9/5.9/8.3GC, KTA19/38GC - SSM558/CM556/CM2358 | CM556 |  | QSC8.3/QSL9 | CM554
 | SSM558 |  |  | CM500
ISB | CM550 |  | QSK19/23/45/60/78 | CM500
ISB - CM850 | CM850 |  | QSK19G/38G/60G, QSV81/91 - CM700/SSM558/CM2358 | CM700, SSM558
ISB Daimler Chrysler | CM551 |  |  | CM2358
ISBe (4 and 6 Cylinder) | CM800 |  | QSM11 | CM570
ISBe2/3 - CM850 | CM850 |  | QST30 | CM552
ISBe4 (4 and 6 cylinder) | CM850 |  | QST30 - Power Gen | CM552
ISC / Transit Bus ISL8.3 - CM850 | CM850 |  | QSX15 | CM570
ISC/ISL | CM554 |  | Signature/ISX | CM570
ISL8.9 - CM850 | CM850 |  | Signature/ISX - CM870 | CM870
ISLe4 (6 cylinder) | CM850 |  |  | 

## Slide 85: Questions or Issues
Please contact Cummins Care for any questions or issues
  Call: 1-800-CUMMINS
  Email: ServiceToolSupport@cummins.com
  Chat Service: www.cummins.com
  Tool Support Website: www.cummins.com
Public